## Slide 1: Digital Logic & Digital Systems Part B Functional Units from Logic Gates & Sequential Logic, Counters and Shift Registers
4004CEM
Computer Architecture & Networks

## Slide 2: Today ….
    Adders & Subtractors
    Comparators
    Decoder & Encoder
    Multiplexer and Demultiplexer
    Registers & Shift Registers

## Slide 3: Digital Circuits
Digital circuits are classified into two categories:
Combinational circuit
The input values explicitly determine the output (the output depends only on the current state of the inputs)
Sequential circuit
The output is a function of the input values and the existing state of the circuit (the output depends on the current state of the inputs and the previous state of the outputs)

## Slide 4: Digital Circuits
Digital circuit operations are described using:
    Boolean expressions
    Logic diagrams
    Truth tables

## Slide 5: Digital Circuits
Boolean expressions: An algebraic notation which is used demonstrate the components and activity of electrical circuits.
Logic diagram: A graphical representation of a circuit. Each type of gate is represented by a specific graphical symbol.
Truth table: A table showing all possible input values and the associated output values.

## Slide 6: Adders
At the digital logic level, addition is performed in binary. Addition operations are carried out by special circuits called, appropriately, adders.
Addition rules:
0
+ 0
0
1
+ 0
1
0
+ 1
1
1
+ 1
10
Add Carry to next bit (if not MSB)

## Slide 7: Half Adder
A circuit that computes the sum of two bits
Truth table
Examine the half adder’s truth table carefully.
  The Sum column has the same results as the XOR gate.
  The Carry column has the same results as the AND gate.

## Slide 8: Half Adder
Circuit diagram
Boolean expressions:
Sum = A  B Carry = AB
Logic symbol

## Slide 9: Binary Addition
1 0 1 0
+ 1 1
(carry)
1
1
0
1
1
1 1 0 1 0
+ 1 1 1 0 0
(carry)
1
0
1
1
0
1
1
(carry)
1
Conceptually similar to decimal addition

## Slide 13: Full Adder
A circuit that takes the carry-in value into account

## Slide 14: Full Adder
A circuit that takes the carry-in value into account
Circuit diagram
Logic symbol

## Slide 15: Parallel Binary Adder
2-bit parallel binary adder
Two or more full adders are connected to form parallel binary adders

## Slide 16: Parallel Binary Adder
Block diagram for 8-bit parallel binary adder
0
A8 A7 A6 A5 A4 A3 A2 A1
B8 B7 B6 B5 B4 B3 B2 B1
_______________________
C8 ∑8 ∑7 ∑6 ∑5 ∑4 ∑3 ∑2 ∑1
To add two 8-bit numbers (A + B), the carry input to the first stage should be 0 and the sum size will be 9-bit at most
C0
+

## Slide 17: Parallel Binary Adder
8-bit parallel binary adder

## Slide 18: Parellel Substractor

## Slide 19: HALF SUBSTRACTOR TRUTH TABLE
Difference similar to XOR output
Borrow = NOR + AND

## Slide 21: Full substractor

## Slide 23: Parallel Binary Subtractor
The subtraction A – B can be done by taking the 2’s complement of B and adding it to A because A - B = A + (-B)
The 2’s complement of B can be calculated by adding 1 to the 1’s complement (convert 0 → 1 and 1 → 0) of binary number B
-B = + 1
Thus, the subtraction A – B can be calculated using the parallel binary adder circuit by complementing all the bits of B and add 1 to the least significant bit (by setting carry C0 to 1)

## Slide 24: Parallel Binary Subtractor
Block diagram for 8-bit parallel binary Subtractor
1
A8 A7 A6 A5 A4 A3 A2 A1
8 7 6 5 4 3 2 1
_______________________
C8 ∑8 ∑7 ∑6 ∑5 ∑4 ∑3 ∑2 ∑1
C0
To subtract two 8-bit numbers (A – B), the first number A should be added to the 2’s complement of the second number (+ 1)
+

## Slide 25: Parallel Binary Subtractor
8-bit parallel binary subtractor

## Slide 26: Comparator
Magnitude Comparator has three output terminals, one each for equality, A = B greater than, A > B and less than A < B.
1-bit Digital Comparator

## Slide 27: Comparator
4-bit Magnitude Comparator

## Slide 28: Decoder
If it is required to read or write data from 4 devices, only one device must be active at a time. To be able to control these 4 devices, each device should be connected to the Control Unit via an individual wire.
The more devices are connected, the more the number of wires!!

## Slide 29: Decoder
Address decoding provides a solution to control the 4 devices using only 2 wires from my Control Unit.

## Slide 30: Decoder
A decoder is a combinational digital circuit with a number of inputs n and a number of outputs 2n.
Only one of the outputs is enabled at a time. The output enabled is the one specified by the binary number formed at the inputs of the decoder.
3-to-8 Decoder
Binary-to-Octal Decoder

## Slide 31: Decoder
2-to-4 Decoder

## Slide 32: Encoder
The opposite of the decoding process.
An encoder has a number of input lines, only one of which is activated at a given time.
Take 2n input lines and generate n output lines.
Decimal-to-BCD Encoder

## Slide 33: Encoder
Octal-to-Binary Encoder

## Slide 34: Switching Network
Multiplexer (MUX)
  Routes one of many inputs to a single output
  Also called a selector
Demultiplexer (DEMUX)
  Routes a single input to one of many outputs
  Also called a distributer
Multiplexer
Demultiplexer
control
control

## Slide 35: Multiplexers
A multiplexer (MUX) has 2n data inputs, n control inputs and one output. The output has always the same value as the data input specified by the binary number at the control inputs.
A television producer wishes to select the output of one of three cameras to go to a monitor.
MUX is used to select which register from the CPU set of registers is connected to the ALU.
Multiplexer Input Line Selection
4-to-1 Multiplexer

## Slide 36: 4-to-1 Multiplexer
4-to-1 Multiplexer

## Slide 37: Demultiplexer
A demultiplexer (DEMUX) has a single input and distributes it over has 2n outputs using n control inputs.

## Slide 38: Demultiplexer
1-to-4 Demultiplexer

## Slide 39: MUX/DEMUX Applications
Sharing complex logic functions such as sharing an adder: MUX select inputs and DEMUX distribute the sum
multiple inputs
multiple output destinations
MUX
A
B
Sum
A0 A1
Ss
Sb
B0 B1
MUX
DEMUX
Z0 Z1
single adder
Sa

## Slide 40: Sequential Circuits

## Slide 41: Sequential Circuits
Digital circuits can also be used to store information.
This application employs sequential circuits, because the output of the circuit is also used as input to the circuit. These circuits are the basic form for designing memory.

## Slide 42: Circuits as Memory
The S-R (Set-Reset) latch is the most basic type. It can be constructed from NOR gates or NAND gates.
NAND Active-LOW Latch NOR Active-HIGH Latch

## Slide 43: SR Latch
An S-R latch stores a single binary digit (1 or 0)
There are several ways an S-R latch circuit can be designed using various kinds of gates

## Slide 44: SR Latch
The design of this circuit guarantees that the two outputs Q and are always complements of each other.
The value of Q at any point in time is considered to be the current state of the circuit.
Therefore, if Q is 1, the circuit is storing a 1; if Q is 0, the circuit is storing a 0.

## Slide 45: NAND Gate Recap
The NAND gate accepts more than one input signal. If all inputs are 1, the output is 0; otherwise, the output is 1

## Slide 46: SR Latch
If R=0 and S=1
S=1
R=0
Q
1
The latch is Reset (Q = 0)
=1
=0

## Slide 47: SR Latch
If R=1 and S=0
S=0
R=1
Q
1
The latch is Set (Q = 1)
=0
=1

## Slide 48: SR Latch
If R=1 and S=1
S=1
R=1
Q
1
The latch stores the old value of Q (Q=1)
=0
=1
0
1 at one of the inputs does not guarantee the value of output. So, the second input has to be tested.
If Q=1

## Slide 49: SR Latch
If R=1 and S=1
S=1
R=1
Q
0
The latch stores the old value of Q (Q=0)
=1
=0
1
1 at one of the inputs does not guarantee the value of output. So, the second input has to be tested.
If Q=0  =1

## Slide 50: SR Latch
Truth Table

## Slide 51: Gated SR Latch
The S and R inputs are only enabled (i.e. affect the circuit) when the clock input is 1. When the clock input is 0, it stores the previous state.

## Slide 52: D-Type Latch
It ensures that inputs S and R are never equal to 1 at the same time

## Slide 53: 4-bit Register

## Slide 54: 4-bit Shift Register
Serial in – Parallel out Shift Register

## Slide 55: Further Reading
Computer Organization and Architecture – Designing for Performance (10th Edition), William Stallings [Chapters: 11]
Digital Fundamentals (11th Edition), Thomas L. Floyd [Chapters: 6, 7, 8, 9]
Computer Organization and Design – The Hardware/Software Interface (5th Edition), David A. Patterson & John L. Hennessy [Appendix: A]
Fundamentals of Computer Architecture, Mark Burrell [Chapter: 4, 5]